## Slide 1
AI-Assisted EEG Screening for
Rapid and Informed Critical Care
TCS-Net · Methodology, Results & Comparative Analysis
Master's Project - Final Presentation
Gagandeep Singh
Spring 2026

## Slide 2
Problem Statement
R
RUTGERS
2
Develop an automated system to detect and classify seizures and other harmful brain activity patterns from EEG recordings of critically ill patients.
The challenges
EEG review is manual and requires specialized neurologists
Experts genuinely disagree on borderline cases
Class imbalance
Soft target — must capture uncertainty, not force a single answer
How an automated tool helps
Probabilities for all 6 patterns simultaneously
Faster insights → timely ICU intervention
Consistent results across reviewers and shifts
Honest uncertainty when experts genuinely disagree

## Slide 3
Our Approach: TCS-Net
R
RUTGERS
3
Temporal Cross Spectrogram Network — raw EEG and dual spectrograms fused via cross-modal attention
Cross-Modal Attention
Bidirectional attention between raw-EEG temporal tokens and spectrogram patches
Frequency Band Gate
EEG context gates spectrogram features across delta / theta / alpha / beta — exploits known neuroscience.
Temperature Scaling
Per-fold post-hoc calibration.
Architectural Intuition
Most of the solution processes EEG and spectrograms independently and concatenates the features. None uses cross-modal attention. TCS-Net's hypothesis: letting the two modalities query each other improves discrimination on patterns that require correlating spatial EEG with frequency content (Spectrograms).

## Slide 4
TCS-Net Architecture (29.6M parameters)
R
RUTGERS
4

## Slide 5
Cross-Modal Token Attention: Step by Step
R
RUTGERS
5
EEG temporal tokens · 50 total
t=0-10s
t=10-20s
t=20-30s
t=30-40s
t=40-50s
delta
theta
alpha
beta
gamma
Spectrogram frequency-band patches · 32 total
EEG → Spec
Spec → EEG
Line thickness = attention weight · highlighted box = querying token
1
Each encoder produces tokens
EEG → 50 temporal tokens (~1s each); spec → 32 frequency-band patches.
2
EEG asks the spectrogram
Each EEG token: "what frequencies are active at my time position?"
3
Spectrogram asks the EEG
Each spec patch: "what waveform shape produces this frequency?"
4
Repeat for 2 layers
Round 2 refines because both sides now have partial cross-modal context.
Like two detectives comparing notes during the investigation.

## Slide 6
Dataset
R
RUTGERS
6
Harvard Medical School / Massachusetts General Hospital — public via Kaggle here (HMS, 2024)
Patients
1,950
broad age, near-balanced sex
Unique EEGs
17,089
200 Hz, 19 electrodes
Labeled segments
106,800
expert-annotated
Six classes — multi-expert vote distribution (~12 experts per recording)
Seizure | 20,933 | LPD — Lateralized Periodic Discharges | 14,856
GPD — Generalized Periodic Discharges | 16,702 | LRDA — Lateralized Rhythmic Delta | 16,640
GRDA — Generalized Rhythmic Delta | 18,861 | Other | 18,808
Bimodal annotation quality: 1–7 votes (noisy) or ≥10 votes (reliable, used as HQ subset)

## Slide 7
Benchmarks: VIPEEGNet & EfficientNetB0
R
RUTGERS
7
Two contrasting baselines, both re-trained on our shared 5-fold patient splits
VIPEEGNet · ~13M params
npj Digital Medicine, 2025
Raw EEG · 16 ch × 10,000 steps
SumToOne Conv1D → pseudo-image
EfficientNetV2-B3 backbone
Global pool → 6-class head
OOF KLD: 0.227
EfficientNetB0 · ~5M params
spectrogram-only baseline
Spectrogram only · 8 ch × 128 × 256
EfficientNetB0 backbone (ImageNet pretrained)
Global avg pool → 6-class head
4-epoch training
OOF KLD: 0.673

## Slide 8
Result: KLD on Shared HQ Subset
R
RUTGERS
8
Lower is better · 5,939 high-quality EEG-IDs (HQ = ≥10 expert votes) · raw softmax outputs across all models
Chart: 
| VIPEEGNet | TCS-Net (ours) | EfficientNetB0
OOF KLD | 0.227 | 0.38 | 0.673
Reading the headline
VIPEEGNet wins, and it wins reliably, its number doesn't change much across different patients.
TCS-Net is meaningfully behind. The gap is big enough that we'd see it on any patient sample. Best amongst 5-folds produces KLD of 0.338.
EfficientNetB0 is both worse and inconsistent on some folds it nearly doubles its own score on others, which is a red flag for clinical deployment regardless of the average.
KLD doesn't tell you what kinds of mistakes each model makes — and that's where the real story is.

## Slide 9
AUROC with statistical evidence
R
RUTGERS
9
What AUROC Answers?
If I randomly pick one real seizure and one non-seizure, what's the chance the model scores the seizure higher?
Per-Modal AUROC (With 95% CI)

## Slide 10
AUPRC reveals the precision gap AUROC dilutes
R
RUTGERS
10
ROC averages over all False Positive(FP) rates, including high-FP regions where the curves crowd into the top-right corner. Precision-recall lives in the regime where false alarms actually hurt, and that's where the differences open up.
Why the gap looks bigger here than on the ROC?
Dashed line = positive prevalence floor (0.059). Every model is well above floor; the ranking gap is real.

## Slide 11
Operating Point Cost
R
RUTGERS
11
At Recall 0.95: VIPEEGNet flags 1,619 false alarms vs 2,263 (EffNetB0) and 2,675 (TCSNet): every model misses 17 of 348 seizures.
At Recall 0.99: EffNetB0 wins: 2,998 FP vs 3,828 (VIP) and 4,505 (TCS). Its hardest seizures are scored less catastrophically low than VIPEEGNet's.
Recall | Model | τ | Sens | Spec | Precision | FN | FP | NNR
0.90 | EffNetB0 | 0.131 | 0.902 | 0.698 | 0.157 | 34 | 1,687 | 6.4
 | TCSNet | 0.021 | 0.902 | 0.732 | 0.173 | 34 | 1,501 | 5.8
 | VIPEEGNet | 0.046 | 0.902 | 0.840 | 0.260 | 34 | 896 | 3.9
0.95 | EffNetB0 | 0.072 | 0.951 | 0.595 | 0.128 | 17 | 2,263 | 7.8
 | TCSNet | 0.012 | 0.951 | 0.522 | 0.110 | 17 | 2,675 | 9.1
 | VIPEEGNet | 0.019 | 0.951 | 0.710 | 0.170 | 17 | 1,619 | 5.9
0.99 | EffNetB0 | 0.035 | 0.991 | 0.464 | 0.103 | 3 | 2,998 | 9.7
 | TCSNet | 0.006 | 0.991 | 0.194 | 0.071 | 3 | 4,505 | 14.1
 | VIPEEGNet | 0.003 | 0.991 | 0.315 | 0.083 | 3 | 3,828 | 12.1

## Slide 12
Recall VS Alert Burden
R
RUTGERS
12
Going from 95 % to 99 % recall is not a free 4 % - it almost doubles the alert burden for every model.
EffNetB0 +735 (+32 %) TCSNet +1,830 (+68 %) VIPEEGNet +2,209 (+136 %)
FA Increase, R 0.95 -> 0.99. :

## Slide 13
Calibration: Are the probabilities trustworthy?
R
RUTGERS
13
TCSNet and VIPEEGNet are already well-calibrated raw, their probabilities can be trusted as-is, and post-hoc calibration adds little. EffNetB0 is severely miscalibrated raw (ECE 0.123) due to a curved, non-uniform overconfidence pattern. Platt scaling fixes it (ECE 0.017, a 7.2× reduction); temperature scaling does not (ECE 0.128) because a single scalar cannot reshape a curve.
Insight

## Slide 14
The Stability Pillar
R
RUTGERS
14
Per-fold τ on log scale. Tighter clusters = more stable across cohorts.
Model | mean ± std | min | max | max / min
EffNetB0 | 0.105 ± 0.058 | 0.041 | 0.199 | 4.9×
TCSNet | 0.013 ± 0.003 | 0.011 | 0.018 | 1.6×
VIPEEGNet | 0.020 ± 0.014 | 0.003 | 0.042 | 12.9×
TCSNet wins on stability. Its R = 0.95 threshold barely moves fold-to-fold, a 1.6× spread is the closest thing to "calibrate once, ship" in this cohort.
VIPEEGNet has the strongest population AUC but the worst drift. Its score distribution shifts fold-to-fold even when the ranking is good, a fixed central τ would over- or under-fire by 13× depending on the cohort.
EffNetB0 sits in the middle (4.9×). Manageable with light per-cohort recalibration.

## Slide 15
Hard misses by threshold: True seizures the model failed to flag
R
RUTGERS
15
A hard miss is a true seizure the model scored BELOW the decision threshold τ, a real seizure that went unflagged.
TCS-Net performed worst amongst all the three modal here, followed by VipeegNet.

## Slide 16
Performance on ambiguous cases
R
RUTGERS
16
This is a reassuring failure pattern, clean seizures are caught reliably; difficult, ambiguous ones are missed with the experts' own uncertainty as a covariate. The models are not failing arbitrarily; they are tracking the underlying difficulty of the label distribution. A clinical AI failing on cases experts could not agree on is a fundamentally different (and more acceptable) failure than one missing clear seizures.

## Slide 17
Verdict
R
RUTGERS
17
Each model wins a different deployment scenario. The decision is not technical — it is institutional.

## Slide 18
Thank you
Questions and discussion
Gagandeep Singh · Master's Project · Spring 2026